What to test
- Accuracy x-axis, y-axis
- Accuracy z-axis
- Accuracy angle
- Speed of the system
  - sending pcd
  - speed of calculation

List of RoboCup objects:
- Axis
- Bearing
- Bearing box
- Big aluminum profile (don’t have)
- Big black profile
- Big nut
- Bolt (Don’ t have)
- Distance tube
- Motor
- R20
- Small aluminum profile
- Small black profile
- Small nut

Checkpoints accuracy x-axis, y-axis test:

Checkpoints X-axis, Y-axis test
X-axis (mm)
Y-axis (mm)

Checkpoints accuracy z-axis test:

Checkpoints accuracy Z-axis test
X-axis, Y-axis (mm)
Z-axis (mm)

Checkpoints accuracy angle test:

Change in Angle(°)	0	30	60	90	120	150	180	210	240	270	300	330

Accuracy x-axis, y-axis
The objects we need for this test:
- Camera
- All RoboCup objects
- Milling machine
- Wooden plank
- Double sided tape

Setup:
We attach the camera to a fixed point of the milling machine so that it can see the movable bed of the milling machine. On top of the bed of the milling machine we put a wooden plank so the bed is level. One of the RoboCup objects gets attached with double sided tape to the wooden plank so it can’ t move while testing. The distance from camera to table needs to be +/-40 cm while running this test.

How to test:
Make a 3d scan of the object when it lays around the middle of the camera view. After this move the bed in the cross pattern (like shown in graph X) and make a scan in every point of this cross pattern. The first result is used as reference. We will move the bed x and y cm. We calculate the difference in the outcome of the results and compare it with the real movements we made to determine the precision of our system.
After all scans are made, attach another RoboCup object to the wooden plank and repeat the same test with this other object. Repeat this for all RoboCup objects.
After the test we can calculate the deviation in x and y-axis of every object.

Results:

Conclusion:

Accuracy z-axis
The objects we need for this test:
- Camera
- All RoboCup objects
- Milling machine
- Wooden plank
- Double sided tape

Setup:
We attach the camera to a fixed point of the milling machine so that it can see the movable bed of the milling machine. On top of the bed of the milling machine we put a wooden plank so the bed is level.

How to test:
Make a 3d scan of just the bed. After this change the height of the bed (like shown in graph Y) and make a scan. Repeat this process for all heights shown in graph Y (range of 20-40 cm table to camera distance). The first result is used as reference. We calculate the difference in the outcome of the results and compare it with the real movements that are made to determine the precision of our system. After the test we can calculate the deviation in z-axis for our system.

Results:

Conclusion:
Accuracy angle
The objects we need for this test:
- Camera
- Multiple RoboCup objects
- Milling machine
- Rotary table
- Wooden plank
- Double sided tape

Setup:
We attach the camera to a fixed point of the milling machine so that it can see the movable bed of the milling machine. On top of the bed of the milling machine we attach a rotary table so we can give the object a known angle. On top of this rotary table we attach the wooden plank so the bed is level. One of the RoboCup objects gets attached with double sided tape to the wooden plank so it can’ t move while testing. The distance from camera to table needs to be +/-40 cm while running this test.

How to test:
Make a 3d scan of the object when it lays around the middle of the camera view. After that change the angle of the bed with the rotary table (Like show in graph Z) and make a new scan. The first result is used as reference. We calculate the difference in the outcome of the results and compare it with the real movements we made to determine the precision of our system.
After all scans are made, attach another RoboCup object to the wooden plank and repeat the same test with this other object. Repeat this for all RoboCup objects.
After the test we can calculate the deviation in angle for our system.

Results:

Conclusion:
Speed of the system
The objects we need for this test:
- Camera
- a RoboCup object

Setup:
Integrate a timer in the code that starts when the code is executed. Print the timer value before and after step/process in the code where the process time needs to be measured. This test will be done on a laptop and is meant to optimize the code and see if it can be more efficient.

How to test:
Use the printed times to calculate the time a process took.

Results:

Conclusion: