Bearing box before pass through filter

Bearing box after pass through filter

With this filter you can define min and max dimensions of x,y,z. In this particular example we use it to remove the curved edges so the segmentation will get easier and more accurate.

Note that the generated PCD file contains a lot of 0 0 0 points. This can give miscalculations when calculating the TF. We saw this happening and this will be fixed.

After removing the 0 0 0 points. The Z height of the TF is level with the table.

Bearing box before Voxel Grid filter

Bearing box after Voxel Grid filter

The Voxel Grid filter is used to reduce the number of points. This decreases computing time.
Little test if watching with an angle to the distance tube makes it more visible. We decided to stick with current setup and make this work before we change things like this.