What to test
- Accuracy x-axis, y-axis
- Accuracy z-axis
- Accuracy angle
- Speed of the system
  - sending pcd
  - speed of calculation
- power consumption software (load on cpu/gpu)?

List of RoboCup objects:
- Axis
- Bearing
- Bearing box
- Big aluminum profile (don’t have)
- Big black profile
- Big nut
- Bolt (Don’ t have)
- Distance tube
- Motor
- R20
- Small aluminum profile
- Small black profile
- Small nut

Checkpoints accuracy x-axis, y-axis test:

Checkpoints X-axis, Y-axis test
Displacement X-axis (mm)
Displacement Y-axis (mm)

Checkpoints accuracy z-axis test:

Checkpoints accuracy Z-axis test
Displacement X-axis, Y-axis (mm)
Displacement Z-axis (mm)

Accuracy x-axis, y-axis
The objects we need for this test:
- Camera
- Multiple RoboCup objects
- Milling machine
- Wooden plank
- Double sided tape

Setup:
We attach the camera to a fixed point of the milling machine so that it can see the movable bed of the milling machine. On top of the bed of the milling machine we put a wooden plank so the bed is level. One of the RoboCup objects gets attached with double sided tape to the wooden plank so it can’ t move while testing. The distance from camera to table needs to be +/-40 cm while running this test.

How to test:
Make a 3d scan of the object when it lays around the middle of the camera view. After this move the bed in the cross pattern (like shown in graph X) and make a scan in every point of this cross pattern. The first result is used as reference. We will move the bed x and y cm. We calculate the difference in the outcome of the results and compare it with the real movements we made to determine the precision of our system.
After all scans are made, attach another RoboCup object to the wooden plank and repeat the same test with this other object. Repeat this for all RoboCup objects.
After the test we can calculate the deviation in x and y-axis of every object.

Results:

Conclusion:

Accuracy z-axis
The objects we need for this test:
- Camera
- Multiple RoboCup objects
- Milling machine
- Wooden plank
- Double sided tape

Setup:
We attach the camera to a fixed point of the milling machine so that it can see the movable bed of the milling machine. On top of the bed of the milling machine we put a wooden plank so the bed is level.

How to test:
Make a 3d scan of just the bed. After this change the height of the bed (like shown in graph Y) and make a scan. Repeat this process for all heights shown in graph Y (range of 20-40 cm table to camera distance). The first result is used as reference. We calculate the difference in the outcome of the results and compare it with the real movements that are made to determine the precision of our system. After the test we can calculate the deviation in z-axis for our system.

Results:

Conclusion:
Accuracy angle
The objects we need for this test:
- Camera
- Multiple RoboCup objects
- Milling machine
- Wooden plank
- Double sided tape

Setup:

How to test:

Results:

Conclusion:
Speed of the system
The objects we need for this test:

Setup:
Integrate a timer in the code that starts when the code is executed. Print the timer value before and after a part of the code where the process time needs to be measured.

How to test:
Use the printed times to calculate the time a process took.

Results:

Conclusion: